## Slide 1: CS433 Parallel and Distributed Computing
Lecture 5 GPU Architecture
Prof. Xiaoyao Liang
2020/9/30

## Slide 2: GPU Scaling
A quiet revolution and potential build-up
  Calculation: 20 TFLOPS vs. 100 GFLOPS
  Memory Bandwidth: 1.6TB/s vs. 16 GB/s
  Every PC, phone, pad has GPU now

## Slide 3: GPU Speedup
GeForce 8800 GTX vs. 2.2GHz Opteron 248
• 10´ speedup in a kernel is typical, as long as the kernel can occupy enough parallel threads
• 25´ to 400´ speedup if the function’s data requirements and control flow suit the GPU and the application is optimized

## Slide 4: GPU Speedup

## Slide 5: Early Graphic Hardware

## Slide 6: Early Electronic Machine

## Slide 7: Early Graphic Chip

## Slide 8: Graphic Pipeline
• Sequence of operations to generate an image
using object-order processing
  Primitives processed one-at-a-time
  Software pipeline: e.g. Renderman
• High-quality and efficiency for large scenes
  Hardware pipeline: e.g. graphics accelerators
• Will cover algorithms of modern hardware pipeline
  But evolve drastically every few years
  We will only look at triangles

## Slide 9: Graphic Pipeline
• Handles only simple primitives by design
  Points, lines, triangles, quads (as two triangles)
  Efficient algorithm
• Complex primitives by tessellation
  Complex curves: tessellate into line strips
  Curves surfaces: tessellate into triangle meshes
• “pipeline” name derives from architecture design
  Sequences of stages with defined input/output
  Easy-to-optimize, modular design

## Slide 10: Graphic Pipeline

## Slide 11: Pipeline Stages
• Vertex processing
  Input: vertex data (position, normal, color, etc.)
  Output: transformed vertices in homogeneous canonical view-volume, colors, etc.
  Applies transformation from object-space to clip-space
  Passes along material and shading data
• Clipping and rasterization
  Turns sets of vertices into primitives and fills them in
  Output: set of fragments with interpolated data

## Slide 12: Pipeline Stages
• Fragment processing
  Output: final color and depth
  Traditionally mostly for texture lookups
• Lighting was computed for each vertex
  Today, computes lighting per-pixel
• Frame buffer processing
  Output: final picture
  Hidden surface elimination
  Compositing via alpha-blending

## Slide 13: Vertex Processing

## Slide 14: Clipping

## Slide 15: Rasterization

## Slide 16: Anti-Aliasing

## Slide 17: Texture

## Slide 18: Gouraud Shading

## Slide 19: Phong Shading

## Slide 20: Alpha Blending

## Slide 21: Wireframe

## Slide 22: SGI Reality Engine (1997)

## Slide 23: Graphic Pipeline Characteristic
• Simple algorithms can be mapped to hardware
• High performance using on-chip parallel execution
  highly parallel algorithms
  memory access tends to be coherent

## Slide 24: Graphic Pipeline Characteristic
• Multiple arithmetic units
  NVidia Geforce 7800: 8 vertex units, 24 pixel units
• Very small caches
  not needed since memory access are very coherent
• Fast memory architecture
  needed for color/z-buffer traffic
• Restricted memory access patterns
  read-modify-write
• Easy to make fast: this is what Intel would love!

## Slide 25: Programmable Shader

## Slide 26: Programmable Shader

## Slide 27: Unified Shader

## Slide 28: GeForce 8

## Slide 29: GT200

## Slide 30: GPU Evolution

## Slide 31: Moore’s Law
Computers no longer get faster, just wider
You must re-think your algorithms to be parallel !
Data-parallel computing is most scalable solution

## Slide 32: GPGPU 1.0
GPU Computing 1.0: compute pretending to be graphics
Disguise data as textures or geometry
Disguise algorithm as render passes
Trick graphics pipeline into doing your computation!
Term GPGPU coined by Mark Harris

## Slide 33: GPU Grows Fast
GPUs get progressively more capable
  Fixed-function ! register combiners ! shaders
  fp32 pixel hardware greatly extends reach
Algorithms get more sophisticated
  Cellular automata ! PDE solvers ! ray tracing
  Clever graphics tricks
High-level shading languages emerge

## Slide 34: GPGPU 2.0
GPU Computing 2.0: direct compute
  Program GPU directly, no graphics-based restrictions
  GPU Computing supplants graphics-based GPGPU
  November 2006: NVIDIA introduces CUDA

## Slide 35: GPGPU 3.0
GPU Computing 3.0: an emerging ecosystem
  Hardware & product lines
  Algorithmic sophistication
  Cross-platform standards
  Education & research
  Consumer applications
  High-level languages

## Slide 36: GPGPU 4.0
GPU Computing 4.0: the ultimate computing platform
  Core of the modern computer system in data center
  Default for AI, Graphic, VR, AR, Scientific etc
  General computing plus special optimization
  Leading the technology node
  Scalable, virtualized, MIG
  Hotspot in frontend research

## Slide 37: GPGPU Platforms

## Slide 38: Fermi

## Slide 39: Fermi Architecture

## Slide 40: SM Architecture

## Slide 41: SM Architecture
• Each Thread Blocks is divided in 32-
thread Warps
  This is an implementation decision, not
  part of the CUDA programming model
• Warps are scheduling units in SM
• If 3 blocks are assigned to an SM and
each Block has 256 threads, how many
Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
  At any point in time, only one of the 24 Warps will be selected for instruction fetch and execution.

## Slide 42: SM Architecture
• SM hardware implements zero overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute the same instruction when selected
• 4 clock cycles needed to dispatch the
same instruction for all threads in a
Warp
  If one global memory access is needed for every 4 instructions
  A minimal of 13 Warps are needed to fully tolerate 200-cycle memory latency

## Slide 43: SM Architecture
• All register operands of all instructions in the Instruction Buffer are scoreboarded
  Instruction becomes ready after the needed values are deposited
  Prevents hazards
  Cleared instructions are eligible for issue
• Decoupled Memory/Processor pipelines
  Any thread can continue to issue instructions until scoreboarding prevents issue
  Allows Memory/Processor ops to proceed in shadow of other waiting Memory/Processor ops

## Slide 44: SM Architecture
• Register File (RF)
  32 KB (8K entries) for each SM
Single read/write port, heavily banked
• TEX pipe can also read/write RF
• Load/Store pipe can also read/write RF

## Slide 45: SM Architecture
  This is an implementation decision, not part of CUDA
  Registers are dynamically partitioned across all blocks/warps assigned to the SM
  Once assigned to a block, the register is NOT accessible by threads in other warps
  Each thread in the same block only access registers assigned to itself

## Slide 46: SM Architecture
• Each SM has 16 KB of Shared Memory
  16 banks of 32bit words
• CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  read and write access
• Not used explicitly for pixel shader
programs
  we dislike pixels talking to each other

## Slide 47: SM Architecture
• Immediate address constants/cache
• Indexed address constants/cache
• Constants stored in DRAM, and cached on chip
  1 L1 per SM
• A constant value can be broadcast to all threads in a Warp
  Extremely efficient way of accessing a value that is common for all threads in a block!

## Slide 48: Bank Conflict
• Shared memory is as fast as registers if there are no bank conflicts
• The fast case:
  If all threads access different banks, there is no bank conflict
  If all threads access the identical address, there is no bank conflict (broadcast)
• The slow case:
  Bank Conflict: multiple threads access the same bank
  Must serialize the accesses
  Cost = max # of simultaneous accesses to a single bank

## Slide 49: Bank Conflict

## Slide 50: CPU & GPU Architecture Outline
CPU
GPU
L2
L1
RF
RF
L1

## Slide 51: Final Thought

## Slide 52: NVIDIA Volta

## Slide 53: Tensor Core